## Slide 1
Axle Load Situation in Pakistan
By:
Consultant: M/s Finite Engineering (Pvt.) Ltd.
November 2021
Notes: AOA everyone. My name is Bilal Shahid Khokhar and I am presenting on behalf of Finite Engineering (Pvt.) Ltd. First of all I would like to thanks NTRC for inviting us to present current Axle Load Situation in the country.

## Slide 2: CONTENTS
  Introduction
  Objectives
  Survey Locations
  Legal Load Limits in Pakistan
  Summary of Results
  Motorways
  National Highways
  Ports and Dry Ports
  Conclusions & Recommendations
Notes: In this presentation, we will start with the introduction and discuss background and need assessment of axle load survey, objectives of axle load survey, survey locations where recent nationwide axle load study was conducted and legal load limits being followed in Pakistan. Afterwards, we will discuss results of axle load study on motorways and national highways. At the end, we will conclude our findings and discuss recommendations regarding axle load.

## Slide 3: Introduction
  Pakistan’s transport system is primarily dependent on road transport. The National Highway and Motorway Network is about 12,800 km long and cater bulk of the goods traffic plying on the roads of Pakistan.
  These vehicle loads are much heavier than the strength of road infrastructure and are major contributor to premature road failure causing un-designed damage to pavement structure, which ultimately leads to an increased maintenance and rehabilitation cost.
  Poor quality roads increase vehicle operating cost and cause time delays and accidents as well.
  The magnitude of damage depends on the number of axles on the vehicle (more axles ensure distribution of gross load over a larger pavement area), axle configuration (single, tandem or tridem), suspension system, tire pressure and the magnitude of load.
Notes: Let start with the introduction.

## Slide 4: Introduction
  Last Axle Load Study was conducted by NTRC in 1995 to assess the degree of overloading on National Highways.
  Since then, i.e. during the last twenty-five years, traffic composition, vehicle configuration and loading regime have considerably changed and now longer and heavier trucks are plying on the roads.
  Besides, traffic volumes on the network have also increased by manifolds since 1995.
  National Transport Research Centre (NTRC) carried out another nationwide Axle Load Study during 2018-2020 on National Highway and Motorway Network using existing weigh stations.
  M/s Finite Engineering (Pvt.) Ltd. et al. were appointed to conduct the study.
  The axle load survey was conducted for 24 hrs. for 07 days at each location.

## Slide 5: Objectives of the Study
  Determining Loading Characteristics on National Highway & Motorway Network.
  Updation of NTRC 1995 study.
  To find out the number of different axle configurations of trucks plying on National Highway & Motorway Network.
  To assess overloading trend on National Highway & Motorway Network.
  Determination of Load Equivalency Factor (LEF).
  To assist Government of Pakistan, National Highway Authority and other road agencies for taking appropriate measures to control overloading.
Notes: The objective of the study

## Slide 6: Survey Locations
Sr. No. | Province | No. of Stations | Motorways | National Highways
1 | Khyber Pakhtunkhwa | 27 | 11 | 16
2 | Punjab | 50 | 30 | 20
3 | Sindh | 12 | - | 12
4 | Balochistan | 17 | - | 17
5 | Northern Areas | 4 | - | 4
Total |  | 110 | 41 | 69
Ports and dry ports |  |  |  | 
Notes: For this, axle load survey was conducted on 110 locations. Out of which 27 were located in KPK, 50 in Punjab, 12 in Sindh, 17 in Balochistan and 4 in Northern Areas. Out of 110, 41 stations were located on motorways and 69 on national highways.

## Slide 7: Legal Load Limits
  The National Highways Safety Ordinance 2000, Pakistan stipulates maximum axle loads as following:
  Front axle – 5.5 tones
  Single axle - 12 tones
  Tandem axle – 22 tones
  Tridem axle – 31 tones
Sr. No. | Axle Configuration | Diagram | Allowable Load Limit (Tons)
1 | 2 Axle Single |  | 17.5
2 | 3 Axle Tandem |  | 27.5
3 | 4 Axle Single Tandem |  | 39.5
4 | 5 Axle Single Tridem |  | 48.5
5 | 5 Axle Tandem Tandem |  | 49.5
6 | 6 Axle Tandem Tridem |  | 58.5
Notes: This slides discuss the current legal load limits being followed in Pakistan. According to National Highway Safety Ordinance (NHSO 2000), maximum axle load for front axle would be 5.5 tons, 12 tons for single axle, 22 ton for tandem axle and 31 tons for tridem axle. The allowable load limit for 2 Axle is 17.5 ton. For 3 Axle it is 27.5 ton. And for 6 Axle, it is 58.5 tons.

## Slide 8: SUMMARY OF RESULTS
Notes: Ok Lets discuss about the results of axle load survey.

## Slide 9: SUMMARY OF RESULTS
  Composition of Truck Traffic Volume by Axle Configuration
Sr. No. | Axle Configuration | Code | NTRC 1995 | 2019
 |  |  | Percentage | Percentage
1 | 2 Axle Single | 1.2 | 68.01 | 35.81
2 | 3 Axle Tandem | 1.22 | 22.42 | 24.79
3 | 3 Axle Single* | 1.2-2 |  | 0.87
4 | 4 Axle Single Tandem | 1.2-22 | 6.41 | 13.32
5 | 4 Axle Tandem Single* | 1.22-2 |  | 0.63
6 | 4 Axle Single* | 1.2+2.2 |  | 0.02
7 | 5 Axle Single Tridem | 1.2-222 | 3.16 | 5.41
8 | 5 Axle Tandem Tandem | 1.22-22 |  | 3.48
9 | 5 Axle Single Single Tandem* | 1.2+2.22 |  | 0.13
10 | 5 Axle Tandem Single Single* | 1.22+2.2 |  | 0.07
11 | 6 Axle Tandem Tridem | 1.22-222 |  | 15.34
12 | 6 Axle Tandem Single Tandem* | 1.22+2.22 |  | 0.15
Total |  |  | 100.00 | 100.00
Notes: This table represents composition of heavy vehicles by distinct axle configuration. It is quite interesting to note that in 1995, 2 Axle Trucks were recorded as 68.01% of the Truck Traffic Volume, which reduced to 35.81% in 2019. 3 Axle Trucks, which were documented as 22.42% in 1995 increased to 25.86% in 2019. The major increase was observed in 6 Axle Trucks, which represents 15.49% of truck traffic volume as compared to <1.9% in 1995.

## Slide 10: SUMMARY OF RESULTS
Sr. No. | Axle Configuration | Permissible Load Limits | Average Load (Tons) | Maximum Load (Ton) | Minimum Load (Ton) | Standard Deviation | Variance
ON ENTIRE ROAD NETWORK |  |  |  |  |  |  | 
1 | 2 Axle Single | 17.5 | 18.42 | 50.12 | 6.33 | 5.46 | 29.85
2 | 3 Axle Tandem | 27.5 | 39.35 | 79.44 | 11.54 | 9.55 | 91.15
3 | 4 Axle Single Tandem | 39.5 | 39.89 | 90.00 | 19.02 | 11.00 | 120.96
4 | 5 Axle Single Tridem | 48.5 | 55.07 | 85.31 | 21.28 | 13.23 | 175.16
5 | 5 Axle Tandem Tandem | 49.5 | 56.49 | 84.31 | 21.85 | 11.99 | 143.74
6 | 6 Axle Tandem Tridem | 58.5 | 72.98 | 110.93 | 22.11 | 13.76 | 189.25
MOTORWAYS |  |  |  |  |  |  | 
1 | 2 Axle Single | 17.5 | 14.07 | 37.67 | 7.02 | 3.36 | 11.27
2 | 3 Axle Tandem | 27.5 | 23.82 | 59.49 | 11.54 | 5.21 | 27.16
3 | 4 Axle Single Tandem | 39.5 | 31.40 | 74.41 | 19.02 | 6.04 | 36.47
4 | 5 Axle Single Tridem | 48.5 | 38.56 | 75.26 | 24.49 | 7.36 | 54.23
5 | 5 Axle Tandem Tandem | 49.5 | 40.54 | 68.34 | 21.85 | 10.19 | 103.93
6 | 6 Axle Tandem Tridem | 58.5 | 49.40 | 95.00 | 22.77 | 8.97 | 80.50
NATIONAL HIGHWAYS |  |  |  |  |  |  | 
1 | 2 Axle Single | 17.5 | 20.00 | 50.12 | 6.33 | 5.22 | 27.23
2 | 3 Axle Tandem | 27.5 | 40.37 | 79.44 | 11.76 | 8.86 | 78.43
3 | 4 Axle Single Tandem | 39.5 | 41.45 | 90.00 | 19.48 | 10.99 | 120.81
4 | 5 Axle Single Tridem | 48.5 | 57.43 | 85.31 | 21.28 | 12.16 | 147.91
5 | 5 Axle Tandem Tandem | 49.5 | 57.74 | 84.31 | 21.87 | 11.20 | 125.55
6 | 6 Axle Tandem Tridem | 58.5 | 75.09 | 110.93 | 22.11 | 12.03 | 144.80
  Avg., Min. & Max. load with Stdev., & var. of each Axle configuration
Notes: This table represents average, minimum and maximum load values carried by each axle configuration on entire road network and separately for motorways and national highways. The results depict that average load carried by each axle configuration on motorways is less than permissible load limits. For example, in case of 5 Axle Single tridem, average load carried by the truck is 38.56 tons against permissible load limit of 48.5 ton. Whereas, the situation got reversed on national highways. The average load carried by trucks on national highways is more than the allowable load limits. It is 20 against 17.5ton for 2 Axle, 40.37 against 27.5 for 3 Axle and 75.09 tons against 58.5 for 6 Axle Truck.

## Slide 11: SUMMARY OF RESULTS
  Distribution of Truck Traffic by Make
Sr. No. | Make | Percentage of Trucks by Make |  |  | 
 |  | 1995 | 2019-20 |  | 
 |  |  | Overall Road Network | Motorways | National Highways
1 | Bedford | 53.00 | 14.98 | 3.80 | 11.18
2 | Nissan | 16.00 | 10.10 | 0.96 | 9.14
3 | Faw |  | 2.13 | 0.07 | 2.06
4 | Hino | 23.00 | 65.83 | 7.80 | 58.03
5 | Isuzu | 5.00 | 2.36 | 0.83 | 1.53
6 | Mercedes |  | 1.66 | 0.26 | 1.40
7 | UD |  | 1.25 | 0.09 | 1.16
8 | Others | 3.00 | 1.69 | 0.28 | 1.41
Total |  | 100.00 | 100.00 |  | 
Notes: This table describes distribution of truck traffic by Make type and comparison with 1995 study. The results depict that percentage of Bedford trucks has reduced to 15% from 53%, the percentage of Hino trucks has increased to 66% from 23% and the percentage of Nissan trucks has reduced to 10% from 16%. Hino constitutes maximum percentage of 65.83% in truck traffic. However, Bedford still holds second position after Hino with 14.98% of truck traffic.

## Slide 12: SUMMARY OF RESULTS
  Distribution of Truck Traffic by Body Type
Chart: 
| Flat | Half | Full | Covered | Container
 | 0.20143 | 0.080845 | 0.43617 | 0.094389 | 0.18717
Notes: This graph represents distribution of truck traffic by body type. For this, we have classified body type in five different categories i-e., Full, Half, Flat, Container and Covered. The results depict that trucks with full body type are plying more on road network with percentage of 43.62, followed by Flat body type having percentage of 20.14 in total. The percentage of trucks with container body type is 18.72% in total.

## Slide 13: SUMMARY OF RESULTS
  Distribution of Truck Traffic by Type
Chart: 
| Truck | Semi Trailer | Tanker
 | 0.61923 | 0.36661 | 0.014158
Notes: The graph represents distribution of truck traffic by type and is classified as Truck, Tanker and Semi-Trailer. The results depict that percentage of trucks is maximum i-e 61.92, followed by semi-trailer with percentage of 36.66. The percentage of tanker is minimum i-e., 1.42%.

## Slide 14: MOTORWAYS
Notes: Ok now, we will discuss about the results of survey on motorways

## Slide 15: MOTORWAYS
  Load distribution on Motorways M-1, M-2 & M-4
Sr. No. | Axle Configuration | Permissible Load Limits | Parameters | Average | M-1 | M-2 | M-4
1 | 2 Axle Single | 17.5 | Min. Load (Tons) | 7.02 | 7.03 | 7.02 | 7.02
 |  |  | Max. Load (Tons) | 37.67 | 37.67 | 30.68 | 26.30
 |  |  | Avg. Load (Tons) | 14.07 | 14.90 | 12.96 | 14.17
 |  |  | %age Overloading | 9.31 | 14.67% | 5.06% | 6.35%
2 | 3 Axle Tandem | 27.5 | Min. Load (Tons) | 11.54 | 11.54 | 12.65 | 11.60
 |  |  | Max. Load (Tons) | 59.49 | 56.07 | 59.49 | 37.89
 |  |  | Avg. Load (Tons) | 23.82 | 23.63 | 23.52 | 24.34
 |  |  | %age Overloading | 11.85 | 10.82% | 18.75% | 4.42%
3 | 4 Axle Single Tandem | 39.5 | Min. Load (Tons) | 19.02 | 19.65 | 20.00 | 19.02
 |  |  | Max. Load (Tons) | 74.41 | 45.88 | 50.56 | 74.41
 |  |  | Avg. Load (Tons) | 31.40 | 32.02 | 29.68 | 33.72
 |  |  | %age Overloading | 4.54 | 6.54% | 1.35% | 7.77%
4 | 5 Axle Single Tridem | 48.5 | Min. Load (Tons) | 24.49 | 31.20 | 24.49 | 38.51
 |  |  | Max. Load (Tons) | 75.26 | 59.66 | 75.26 | 47.30
 |  |  | Avg. Load (Tons) | 38.56 | 41.13 | 37.06 | 43.22
 |  |  | %age Overloading | 4.04 | 7.69% | 3.03% | 0.00%
5 | 5 Axle Tandem Tandem | 49.5 | Min. Load (Tons) | 21.85 | 41.22 | 24.79 | 21.85
 |  |  | Max. Load (Tons) | 68.34 | 53.02 | 48.83 | 68.34
 |  |  | Avg. Load (Tons) | 40.54 | 46.64 | 36.05 | 46.79
 |  |  | %age Overloading | 9.68 | 25.00% | 0.00% | 22.22%
6 | 6 Axle Tandem Tridem | 58.5 | Min. Load (Tons) | 22.77 | 25.80 | 23.53 | 22.77
 |  |  | Max. Load (Tons) | 95.00 | 70.10 | 60.87 | 95.00
 |  |  | Avg. Load (Tons) | 49.40 | 54.24 | 44.14 | 48.57
 |  |  | %age Overloading | 7.99 | 9.32% | 8.33% | 7.42%
Notes: This table represents load distribution on motorways M-1, M-2 and M-4. During survey it was noted that overloaded trucks were not allowed to enter on Motorways. As stated earlier, average load carried by trucks of each axle configuration is less than allowable load limits. Regarding each of the motorway M-1, M-2 and m-4, the average load carried by 2 Axle truck on M-1 is 14.90 ton, for M-2 it is 12.96 ton and for M-4, average load carried is 14.17 ton. Similarly, for 6 Axle trucks, average load of 54.24 ton was recorded on M-1, 44.14 tons on M-2 and 48.57 tons on M-4.

## Slide 16: MOTORWAYS
  Rear Axle Load Spectra on Motorways
Sr. No. | Range (Tonnes) | Total | Percentage | Cum. Percentage | Percentage above Range Value
1 | 0 - 8.16 | 3467 | 36.38 | 36.38 | 63.62
2 | 8.17 - 9.99 | 2601 | 27.30 | 63.68 | 36.32
3 | 10 - 10.99 | 1321 | 13.86 | 77.54 | 22.46
4 | 11 - 11.99 | 1043 | 10.95 | 88.49 | 11.51
5 | 12 - 12.99 | 601 | 6.31 | 94.79 | 5.21
6 | 13 - 13.99 | 250 | 2.62 | 97.42 | 2.58
7 | 14 - 14.99 | 112 | 1.18 | 98.59 | 1.41
8 | 15 - 19.99 | 117 | 1.23 | 99.82 | 0.18
9 | 20 & Above | 17 | 0.18 | 100.00 | 0.00
Notes: While analyzing rear axle load spectra for Motorways, the results illustrates that 88.49% of axle have load less than 12 tons. Only 11.51% of axles carry out load more than 12 tons.

## Slide 17: MOTORWAYS
  Damage Factors for Major Axle Configuration on Motorways
Sr. No. | Axle Configuration | Code | Damage Factor | 
 |  |  | Road Note 40 | AASHTO 1993
1 | 2 Axle Single | 1.2 | 3.66 | 2.94
2 | 3 Axle Tandem | 1.22 | 6.80 | 3.32
3 | 4 Axle Single Tandem | 1.2-22 | 7.85 | 5.32
4 | 5 Axle Single Tridem | 1.2-222 | 11.30 | 6.29
5 | 5 Axle Tandem Tandem | 1.22-22 | 15.77 | 6.67
6 | 6 Axle Tandem Tridem | 1.22-222 | 10.86 | 5.38
  Damage Factors based on Allowable Permissible Loads
Sr. No. | Axle Configuration | Code | Damage Factor | 
 |  |  | Road Note 40 | AASHTO 1993
1 | 2 Axle Single | 1.2 | 5.71 | 4.56
2 | 3 Axle Tandem | 1.22 | 7.06 | 4.53
3 | 4 Axle Single Tandem | 1.2-22 | 13.22 | 8.89
4 | 5 Axle Single Tridem | 1.2-222 | 14.19 | 8.69
5 | 5 Axle Tandem Tandem | 1.22-22 | 15.17 | 8.87
6 | 6 Axle Tandem Tridem | 1.22-222 | 16.15 | 8.66
Notes: As stated earlier, one of the objective of axle load survey is to calculate damage factors or load equivalency factors. For that, following two approaches including Road Note 40 and AASHTO 1993 were opted. These factors will be used for calculating ESALs in pavement design. The table presents that for 2-Axle, LEF 2.94 …………… -. The second table provides LEF based on allowable permissible loads. It is noteworthy that actual damage factors of vehicles plying on Motorways are reasonably lower than damage factors calculated on allowable load limits.

## Slide 18: MOTORWAYS
  Commodities carried by Truck Traffic on Motorways
Chart: 
| Agriculture Items | Food Items | Animals and Animal Products | Raw Materials | Bulk Manufactures | Basic Manufactures | Miscellaneous Manufactures | Mining and Quarrying | Fuel, Lubricants (Minerals) | Miscellaneous Goods not Classified | Empty
 | 0.099198 | 0.18547 | 0.048373 | 0.066206 | 0.17677 | 0.10834 | 0.10633 | 0.068881 | 0.090727 | 0.037896 | 0.011815
Notes: The commodities carried by heavy vehicles is classified in different categories including Raw materials, Agriculture items, food items, basic manufacturers etc. On motorways, the results illustrates that percentage of food items carried by heavy traffic is maximum i-e., 18.55%, followed by bulk manufactures with percentage of 17.68.

## Slide 19: MOTORWAYS
  Tire Pressure for Major Axle Configuration on Motorways
  As per NHSO 2000, tire pressure for front and rear axle is:
  Front Axle = 100 PSI
  Rear Axle = 120 PSI
Sr. No. | Axle Configuration | Code | Average Pressure (Psi) |  |  |  |  | 
 |  |  | Front | Rear 1 | Rear 2 | Rear 3 | Rear 4 | Rear 5
1 | 2 Axle Single | 1.2 | 130.24 | 144.79 |  |  |  | 
2 | 3 Axle Tandem | 1.22 | 138.50 | 150.54 | 151.47 |  |  | 
3 | 4 Axle Single Tandem | 1.2-22 | 136.50 | 149.84 | 152.31 | 152.45 |  | 
4 | 5 Axle Single Tridem | 1.2-222 | 136.56 | 146.24 | 151.34 | 152.42 | 152.63 | 
5 | 5 Axle Tandem Tandem | 1.22-22 | 139.64 | 148.57 | 149.64 | 153.75 | 154.64 | 
6 | 6 Axle Tandem Tridem | 1.22-222 | 133.64 | 152.76 | 149.69 | 151.95 | 152.29 | 152.63
Notes: This slide describes tire pressure recorded during survey for each axle configuration. As per NHSO (2000), tire pressure for front axle should be 100psi and for rear axle, it should be 120 psi. However, the results depict that tires of vehicles were over-inflated far in excess of their normal pressure capacity on motorways. In case of front axle tire pressure is around 130 to 139 psi, whereas in rear axles it is around 144 to 153 psi.

## Slide 20: NATIONAL HIGHWAYS
Notes: That's all for the motorways, Now we will discuss about the results of survey on national highways.

## Slide 21: NATIONAL HIGHWAYS
Sr. No. | Axle Configuration | Load Limits | Parameters | Total Load (Tons) |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | Avg. | N-5 | N-10 | N-15 | N-25 | N-35 | N-40 | N-45 | N-55 | N-65 | N70 | N-75 | N-80 | N-85
1 | 2 Axle Single | 17.5 | Min. Load | 6.33 | 6.33 | 6.85 | 6.78 | 6.79 | 6.74 | 6.94 | 6.72 | 6.50 | 8.68 | 7.17 | 9.77 | 6.75 | 7.26
 |  |  | Max. Load | 50.12 | 40.85 | 26.12 | 26.45 | 26.70 | 37.28 | 25.62 | 27.79 | 50.12 | 35.00 | 33.24 | 9.77 | 25.43 | 31.81
 |  |  | Avg. Load | 20.00 | 20.45 | 17.55 | 16.43 | 17.84 | 21.77 | 18.07 | 17.73 | 21.71 | 20.59 | 20.17 | 9.77 | 18.56 | 18.32
 |  |  | Overloading (%) | 74.10 | 77.04 | 64.78 | 50.98 | 69.11 | 73.44 | 68.12 | 57.57 | 79.54 | 79.00 | 73.27 | 0.00 | 75.63 | 68.67
2 | 3 Axle Tandem | 27.5 | Min. Load | 11.76 | 11.76 | 12.16 | 12.34 | 12.27 | 12.20 | 12.37 | 12.39 | 12.46 | 15.20 | 12.42 | 21.85 | 12.47 | 12.37
 |  |  | Max. Load | 79.44 | 79.44 | 55.65 | 50.29 | 53.74 | 62.21 | 57.31 | 55.22 | 69.80 | 60.00 | 60.70 | 45.05 | 54.88 | 58.50
 |  |  | Avg. Load | 40.37 | 40.81 | 38.42 | 34.28 | 40.03 | 37.12 | 37.79 | 35.12 | 42.58 | 41.28 | 44.58 | 39.58 | 35.81 | 41.75
 |  |  | Overloading (%) | 90.62 | 93.34 | 94.01 | 71.52 | 87.25 | 75.82 | 87.55 | 87.73 | 94.19 | 85.79 | 89.01 | 85.71 | 89.18 | 93.26
3 | 4 Axle Single Tandem | 39.5 | Min. Load | 19.48 | 19.48 | 19.97 | - | 20.00 | 20.13 | 19.94 | 34.69 | 20.37 | 20.10 | 26.70 | - | 19.52 | 28.41
 |  |  | Max. Load | 90.00 | 90.00 | 55.71 | - | 60.20 | 61.68 | 58.60 | 50.60 | 74.36 | 70.00 | 59.29 | - | 62.29 | 59.84
 |  |  | Avg. Load | 41.45 | 40.85 | 46.15 | - | 50.05 | 41.01 | 45.12 | 42.57 | 42.29 | 40.09 | 47.19 | - | 47.66 | 48.22
 |  |  | Overloading (%) | 57.87 | 54.84 | 81.25 | 0.00 | 95.65 | 59.32 | 91.67 | 75.00 | 58.16 | 50.60 | 89.47 | 0.00 | 88.79 | 88.14
4 | 5 Axle Single Tridem | 48.5 | Min. Load | 21.28 | 21.32 | - | - | 21.46 | 21.44 | 21.28 | 56.97 | 30.01 | 35.86 | 51.20 | - | 48.09 | 49.30
 |  |  | Max. Load | 85.31 | 85.31 | - | - | 78.60 | 83.66 | 75.02 | 67.14 | 79.13 | 79.00 | 61.20 | - | 66.24 | 80.37
 |  |  | Avg. Load | 57.43 | 57.00 | - | - | 65.54 | 59.99 | 48.95 | 62.10 | 57.42 | 57.19 | 54.48 | - | 55.96 | 61.49
 |  |  | Overloading (%) | 79.45 | 76.23 | 0.00 | 0.00 | 97.44 | 75.00 | 68.75 | 100.0 | 79.31 | 85.37 | 100.0 | 0.00 | 90.70 | 100.00
5 | 5 Axle Tandem Tandem | 49.5 | Min. Load | 21.87 | 21.87 | 52.23 | - | 50.09 | 44.62 | 53.76 | 53.99 | 24.75 | 40.56 | 53.66 | - | 43.52 | 50.89
 |  |  | Max. Load | 84.31 | 84.31 | 61.23 | - | 77.72 | 74.29 | 65.43 | 59.49 | 81.43 | 80.00 | 57.62 | - | 71.08 | 76.91
 |  |  | Avg. Load | 57.74 | 57.88 | 56.71 | - | 61.98 | 53.18 | 57.57 | 56.22 | 53.86 | 57.84 | 55.01 | - | 58.31 | 59.28
 |  |  | Overloading (%) | 77.97 | 78.29 | 100.0 | 0.00 | 100.0 | 71.43 | 100.0 | 100.0 | 50.00 | 50.00 | 100.0 | 0.00 | 75.56 | 100.00
6 | 6 Axle Tandem Tridem | 58.5 | Min. Load | 22.11 | 22.67 | 22.78 | 60.89 | 58.89 | 42.85 | 22.87 | 61.29 | 39.28 | 45.00 | 62.11 | - | 58.29 | 22.11
 |  |  | Max. Load | 110.93 | 106.27 | 90.39 | 78.51 | 104.61 | 103.89 | 110.93 | 91.51 | 105.59 | 100.00 | 102.11 | - | 95.29 | 99.20
 |  |  | Avg. Load | 75.09 | 74.10 | 79.02 | 70.63 | 81.38 | 63.60 | 78.60 | 81.05 | 80.80 | 78.23 | 83.04 | - | 78.65 | 79.63
 |  |  | Overloading (%) | 89.04 | 88.39 | 95.83 | 100.0 | 100.0 | 46.4 | 93.88 | 100.0 | 92.92 | 95.16 | 100.0 | 0.00 | 99.25 | 96.55
  Load distribution on National Highways
Notes: The same table representing load distribution on each of the national highway of Pakistan. The results illustrates that average load carried by each axle configuration is more than allowable load limits.

## Slide 22: NATIONAL HIGHWAYS
  Overloading on National Highways
Chart: Axle Configuration
| 2 Axle Single | 3 Axle Tendem | 4 Axle Single Tendem | 5 Axle Single Tridem | 5 Axle Tendem Tendem | 6 Axle Tendem Tridem
% of Trucks carrying Load Under Permissible Load Limits | 0.259 | 0.09381 | 0.42126 | 0.2055 | 0.22025 | 0.10956
% of Trucks carrying Load Over Permissible Load Limits | 0.741 | 0.90619 | 0.57874 | 0.7945 | 0.77975 | 0.89044
Notes: Like for example, in case of 2 Axle, 74.10% of the trucks are overloaded. In 3 axle, 90.62% of trucks are overloaded. Similarly, for 6 Axle, 89.04% of trucks are overloaded.

## Slide 23: NATIONAL HIGHWAYS
  The percentage of overloading on each National Highway is provided below:
Highway | Overloading Percentage
N-5 | 80.20
N-10 | 80.70
N-15 | 61.69
N-25 | 84.81
N-35 | 69.33
N-40 | 83.76
N-45 | 70.54
Highway | Overloading Percentage
N-55 | 86.40
N-65 | 81.78
N-70 | 85.92
N-75 | 75.00
N-80 | 85.61
N-85 | 84.82
Notes: These tables deliberates the percentage of overloading on each of the individual national highway. It is noted that N-5 which is the major national highway of Pakistan and is carrying major freight traffic from Karachi to Torkham is dealing with 80% overloaded heavy vehicles. N-55 is another major national Highway of Pakistan and percentage of overloading on it is 86%. Averaged out, 80% of the heavy vehicles plying on national highways of Pakistan carry load more than allowable load limits.

## Slide 24: NATIONAL HIGHWAYS
  Rear Axle Load Spectra on National Highways
Sr. No. | Range (Tonnes) | Total | Percentage | Cum. Percentage | Percentage above Range Value | %age above Range Value in 1995
1 | 0 - 8.16 | 4689 | 6.36 | 6.36 | 93.64 | 88.18
2 | 8.17 - 9.99 | 5968 | 8.09 | 14.45 | 85.55 | 73.61
3 | 10 - 10.99 | 5098 | 6.91 | 21.37 | 78.63 | 60.69
4 | 11 - 11.99 | 6016 | 8.16 | 29.53 | 70.47 | 43.33
5 | 12 - 12.99 | 8963 | 12.16 | 41.68 | 58.32 | 27.65
6 | 13 - 13.99 | 9204 | 12.48 | 54.16 | 45.84 | 15.49
7 | 14 - 14.99 | 8548 | 11.59 | 65.76 | 34.24 | 8.98
8 | 15 - 19.99 | 22048 | 29.90 | 95.66 | 4.34 | 0.42
9 | 20 & Above | 3202 | 4.34 | 100.00 | 0.00 | 0.00
Notes: While analyzing rear axle load spectra for national highways, the results illustrates that 70.47% of axle carry load more than 12 tons which was only 43.33% in 1995.

## Slide 25: NATIONAL HIGHWAYS
  Damage Factors for Major Axle Configuration on National Highways
Sr. No. | Axle Configuration | Code | Damage Factor (2019) |  | Damage Factor (1995) | 
 |  |  | Road Note 40 | AASHTO 1993 | Road Note 31 | AASHTO 1986
1 | 2 Axle Single | 1.2 | 19.62 | 12.28 | 6.49 | 4.67
2 | 3 Axle Tandem | 1.22 | 55.24 | 23.08 | 18.48 | 8.84
3 | 4 Axle Single Tandem | 1.2-22 | 26.80 | 14.88 | 17.30 | 10.35
4 | 5 Axle Single Tridem | 1.2-222 | 44.66 | 19.02 | - | -
5 | 5 Axle Tandem Tandem | 1.22-22 | 39.35 | 18.42 | 19.59 | -
6 | 6 Axle Tandem Tridem | 1.22-222 | 70.05 | 24.68 | 27.96 | 10.90
Notes: The damaged factors as calculated for national highways are high. In 1995, LEF for 2 Axle was 4.67 which is increased to 12.28 in 2019. For 3 Axle it was 8.84 back in 1995 and now it is increased to 23.08. For 6 Axle, the damaged factors is increased to 24.68 from 10.90.

## Slide 26: NATIONAL HIGHWAYS
  Commodities carried by Truck Traffic on National Highways
Chart: 
| Agriculture Items | Food Items | Animals and Animal Products | Raw Materials | Bulk Manufactures | Basic Manufactures | Miscellaneous Manufactures | Mining and Quarrying | Fuel, Lubricants (Minerals) | Miscellaneous Goods not Classified | Empty
 | 0.1024 | 0.26382 | 0.010922 | 0.041204 | 0.12799 | 0.099702 | 0.0453 | 0.15946 | 0.074252 | 0.061999 | 0.012953
Notes: On national highways, the results illustrates that percentage of food items carried by heavy traffic is maximum i-e., 26.38%, followed by mining and quarrying with percentage of 15.95.

## Slide 27: NATIONAL HIGHWAYS
  Tire Pressure for Major Axle Configuration on National Highways
Sr. No. | Axle Configuration | Code | Average Pressure (Psi) |  |  |  |  | 
 |  |  | Front | Rear 1 | Rear 2 | Rear 3 | Rear 4 | Rear 5
1 | 2 Axle Single | 1.2 | 138.49 | 155.79 |  |  |  | 
2 | 3 Axle Tandem | 1.22 | 143.87 | 158.62 | 159.25 |  |  | 
3 | 4 Axle Single Tandem | 1.2-22 | 146.55 | 158.64 | 159.47 | 159.94 |  | 
4 | 5 Axle Single Tridem | 1.2-222 | 141.70 | 159.91 | 160.16 | 161.20 | 161.93 | 
5 | 5 Axle Tandem Tandem | 1.22-22 | 138.11 | 160.04 | 157.13 | 160.84 | 163.10 | 
6 | 6 Axle Tandem Tridem | 1.22-222 | 149.58 | 161.52 | 162.30 | 163.17 | 163.35 | 163.82
1995 |  |  |  |  |  |  |  | 
1 | 2 Axle Single | 1.2 | 109.08 | 127.67 |  |  |  | 
2 | 3 Axle Tandem | 1.22 | 124.66 | 137.77 | 137.91 |  |  | 
3 | 4 Axle Single Tandem | 1.2-22 | 118.06 | 137.36 | 137.36 | 137.36 |  | 
4 | 5 Axle Single Tridem | 1.2-222 |  |  |  |  |  | 
5 | 5 Axle Tandem Tandem | 1.22-22 |  |  |  |  |  | 
6 | 6 Axle Tandem Tridem | 1.22-222 | 129.17 | 132.33 | 133.06 | 132.91 | 133.33 | 132.92
Notes: The tire pressure of the vehicles as recorded on national highways are far in excess from normal range. In case of front axle tire pressure is around 138 to 149 psi, whereas in rear axles it is around 155 to 163 psi. While comparing with 1995 study, the tire pressure was within the range of 109 to 129 psi for front axle and 127 to 137 psi for rear axle.

## Slide 28: PORTS AND DRY PORTS
Sr. No. | Axle Configuration | Code | Percentage overloading | 
 |  |  | PORTS AND DRY PORTS | National Highways
1 | 2 Axle Single | 1.2 | 46.51 | 74.10
2 | 3 Axle Tandem | 1.22 | 84.49 | 90.62
3 | 4 Axle Single Tandem | 1.2-22 | 55.26 | 57.87
4 | 5 Axle Single Tridem | 1.2-222 | 33.33 | 79.45
5 | 5 Axle Tandem Tandem | 1.22-22 | 94.74 | 77.97
6 | 6 Axle Tandem Tridem | 1.22-222 | 90.56 | 89.04

## Slide 29: CONCLUSIONS
Notes: So, lets conclude our findings now.

## Slide 30: CONCLUSIONS
  The composition of truck traffic is almost entirely changed from the survey carried out in 1995 by NTRC. The main changes are;
  Transition from 2 Axle trucks; in 1995, 2 axle trucks were recorded as 68.9% of the Truck Traffic Volume, which has reduced to half i.e. 35.81% in 2019.
  Fixed body trucks constitute around 61.5% of truck fleet, down from more than 90% in 1995.
  Proportion of Bedford trucks reduced from more than half of truck population i.e. from 53% to just 15%. However, Bedford still constitutes 50% in 2-axle segment.
  Hino make now constitute 2/3 of truck fleet, 66% from 23% in 1995. The percentage of Hino trucks on Motorways and National Highways is 55.39% and 67.54% respectively.
  Transition towards multi-axle semi-trailers (4,5 & 6 axle) which now constitute almost 40% of truck fleet as compared to less than 10% in 1995; a significant increase was observed in 4 & 6 Axle Trucks, which now represent 13.3% and 15.5% of truck traffic volume respectively, as compared to 6.5% and <1.9% in 1995. The share of 3-axle tandem increased marginally.

## Slide 31: CONCLUSIONS
  On National Highways due to lax axle load control regime, severe overloading was observed. The average load carried by trucks of different category (Axle configuration) on National Highways is much higher than allowable legal load limits, ensuing high damage factors, causing rapid deterioration / failure of roads, much before completion of design life.

## Slide 32: RECOMMENDATIONS
Notes: Lets discuss some recommendations based on current axle old situation in the Pakistan.
.

## Slide 33: RECOMMENDATIONS
  Road network carries 96% of freight traffic; therefore a modal shift from road to rail is needed as envisaged in the National Transport Policy and National Transport Master Plan (2020-2029).
  Overloading of vehicles beyond permissible limits is an offence under the Motor Vehicle Ordinance 1965 and National Highway Safety Ordinance 2000, punishable by fine and imprisonment. The 6th Schedule of NHSO 2000 governing gross and axle load limits needs to be uniformly implemented all across the country.
  Provincial governments need to incorporate 6th schedule of NHSO-2000 into provincial Motor Vehicle laws as provincial highway network is around 500,000 km long against 13,000 km of federal government.
  At source control of overloading is important, like at ports, industrial and agricultural centres etc., as it greatly limits overloading and damage inflicted to the pavement. Therefore, weigh stations should be strategically located near the load generating centres.
  All weigh stations along the National Highway and Motorway network be made operational.

## Slide 34: RECOMMENDATIONS
  A National consensus is needed for implementation of the Axle Load Regime (ALR) and consultation with stakeholders like Agriculture, Commerce, Industry, Business, Truckers etc. needs to be established. To achieve consensus a national level committee be constituted with representation of all stakeholders.
  Truck body retrofitting / manufacturing is not regulated and unauthorized and illegal manufacturers are spread all over the country, which strengthen truck bodies to carry loads much beyond their rated capacity.
  Truck, semi-trailer, trailer registration system is out-dated and these vehicles are being registered without any classification, fitness checks, verification etc.
  New types of trucks with different axle configuration have entered the freight market and thus updation of NHSO 2000 is needed.
  A new trucking policy needs to be formulated (i.e. the 2007 trucking policy needs to be updated).

## Slide 35
  Thank You!